## Slide 1: VFd: QoS
And Maybe a Little Mirroring
March 2017
A visual representation of the work by KJ, Alex and Scott, for discussion purposes.
Contact for slides: Henry Fowler

## Slide 2: Purpose
Testing NIC QoS features, and managing them in practice, requires a mechanism for configuration.
Each vendor may have its own unique tools that we can use for lab testing, but a vendor-independent mechanism is preferred longer term for deployment
    VFd has an initial structure for QoS
These slides and diagrams are an attempt to expand on the ASCII figures shown in https://github.com/att/vfd/blob/master/doc/qos/vfd_features_1.md
These seem to assume that an Ethernet VLAN is used between the TOR and the NIC, and the VLAN value is used to assign to the appropriate VF
    Looking to the future, if MPLS is used without Ethernet, this approach would need to be extended, correct?

## Slide 3: VFd QoS – Treatment of Received Packets Point of view from a single VM
VM 0
VF 0
VM i
VF i
TC3
TC2
TC1
TC0
VM n
VF n
Received Ethernet Frame, which includes PCP
Select RX TC queue based on PCP
NIC
Server
VF driver is in VM
Legend:
TC: Traffic Class
RX: Inbound to VM
TX: Outbound from VM
TC3
TC2
TC1
TC0
RX queues
VFd configures the NIC. In addition, the PF responds via mailbox replies to queries from the VF driver
Notes: These figures are an attempt to expand on the ASCII figures shown in:
https://github.com/att/vfd/blob/master/doc/qos/vfd_features_1.md

## Slide 4: VFd QoS – Treatment of Packets Transmitted from the VM Point of view from a single VM (Tenant View)
VM 0
VF 0
VM i
VF i
TC3
TC2
TC1
TC0
VM n
VF n
TX packet
Queue related to TC is chosen, by rules applied by VM
Each TC has a min_bw and a max_bw.
NIC
Server
TC3
TC2
TC1
TC0
TX queues
Treatment is based on the queue, but marking from the VM is passed through and not remarked.
This is a current NIC limitation, and better mechanisms would be desired so we do not have to accept whatever the VM marks.

## Slide 5: VFd QoS – Treatment of Packets Transmitted from the VM Point of view of the NIC card (“system view”)
VM 0
VM i
TC3
TC2
TC1
TC0
TC3
TC2
TC1
TC0
VM n
TX packet
Total of min <= total of max
Each TC has a min_bw and a max_bw that can vary by VF (but does not need to)
NIC
Server
Max_bw_0 Min_bw_0
Max_bw_i Min_bw_i
Max_bw_n Min_bw_n
TC0 values for VF i
The max total # of policers is 4n. 2 rate, 2 color today. But 2R3C would be nice; ability to remark.
TC0 values for VF 0
Notes: 2R3C would be nice; ability to remark.
Also allows WRED – but do we need? (would be on the RX side)

## Slide 6: So what QoS parameters need to be configured by VFd?
Scott have a list already?
With n VFs and m TCs, there would be n*m policers.
    Each policer would have a min and a max.
However, in the management of these policers, at times it will be advantageous to specify a value for a card that applies to multiple policers.

## Slide 7: Two Different Models
How different are they?

## Slide 8: VFs on a 2-port NIC
NIC
Server
10G
Port 1
Port 2
VF 0
VF 1
VF 2
VF 0
VF 1
VF 2
In this case, assume max for each VF is 10G
Min 2G
Min 2G
Min 6G
Assuming the sum of the mins = 10G

## Slide 9: Traffic Classes within a VF
VM i
TC3
TC2
TC1
TC0
NIC
Server
10G
Port 1
Port 2
VF 0
VF 1
VF 2
VF 0
VF 1
VF 2
Min = 6G, max = 10G
TC 3
TC 2
TC 1
TC 0
Each TC has a min guaranteed BW, and a max allowed BW

## Slide 10: Or is the model that each TC has multiple VFs? (And in the end, does it matter?)
NIC
Server
Port 1
Port 2
TC 3
TC 2
TC1
VF0
VFi
TCn
Each TC has a min guaranteed BW, and a max allowed BW
VM 0
VM i
TC3
TC2
TC1
TC0
VM n
TC0 values for VF 0
TC0
TC 3
TC 2
TC1
TC0